SHViT zerlegt

---
16x16 Overlap PatchEmbebed
256 x 256 x 28
32 x 32 x 224
Probe: 32*16 = 512
128 x 128 x 56
64 x 64 x 112
3x3 kernel
Stride = 2
BN
Activation = ReLU
3x3 kernel
Stride = 2
BN
Activation = ReLU
3x3 kernel
Stride = 2
BN
Activation = ReLU
3x3 kernel
Stride = 2
BN
Activation = ReLU
512 x 512 x 3
16x16 Overlap Patch Embed
3x3 strided Conv
3x3 strided Conv
3x3 strided Conv
3x3 strided Conv
[Speaker Notes: 10 - LeViT: a Vision Transformer in ConvNet’s Clothing for Faster Inference: Nutzen auch „4 layers of 3 × 3 convolutions (stride 2)” For LeViT, each convolution is followed by a batch normalization 27 - EfficientViT: Memory Efficient Vision Transformer with Cascaded Group Attention ====================================== - ViT zerlegt das Eingabebild in p×p non-overlapping Patches, die als Eingabe für den Transformer-Encoder dienen. Dies wird standardmäßig mit einer p×p-convolution mit Stride p=16 umgesetzt ====================================== 32 - Early Convolutions Help Transformers See Better Convolutional stem details Our convolutional stem designs use four […] 3×3 convolutions “The output channel“ is “[64, 128, 128, 256, 256, 512]“# All 3×3 convolutions are followed by batch norm (BN) [21] and then ReLU [29]]

---
Stage 1
3x3 DW Conv
Feed Forward Network
3x3 kernel
Stride = ?? Auch 2??
BN (fused)
Activation = ReLU
3x3 kernel ??
Stride = ??
BN (fused)
Activation = ReLU
Fully Connected
32 x 32 x 224
32 x 32 x 224
[Speaker Notes: Batch Normalization ----------------------- Im Bild wird erwähnt, dass Batch Normalization in Convolution Layers integriert (fused) werden kann Während des Trainings wird BN normal verwendet (normalisiert die Ausgabe der Convolution), um die Aktivierungen zu stabilisieren. Wo BN verwendet wird: - In der Abbildung wird BN klar an den Stellen gezeigt, wo 3x3 Depthwise Convolution vorkommt (Stage 1 bis Stage 3) - Für andere Schichten, wie die Feedforward Layers, wird BN verwendet, sofern sie keine Self-Attention-Layer sind. ============================================================================ 10 - LeViT: a Vision Transformer in ConvNet’s Clothing for Faster Inference: - The ViT uses layer normalization before each at- tention and MLP unit - For LeViT, each convolution is followed by a batch normalization - The batch normalization can be merged with the preceding convolution for inference, which is a runtime advantage over layer Normalization 27 - EfficientViT: Memory Efficient Vision Transformer with Cascaded Group Attention 28 - MetaFormer Is Actually What You Need for Vision 29 - Rethinking Mobile Block for Efficient Attention-based Models 32 - Early Convolutions Help Transformers See Better 52 - Batch Normalization: Accelerating Deep Network Training by Reducing Internal Covariate Shift]

---
DownSample
Downsample
[Speaker Notes: 10 – Downsampling 00 downsampling layer, which is composed of two stage 1 blocks, with an inverted residual block [27,50,51] (stride-2) placed between them. Finally, the global average pooling and fully connected layer are used to output the predictions.]

---
Stage 2
3x3 DW Conv
Layer Norm
SH Attention
Feed Forward Network
BatchNorm

---
DownSample

---
Stage 3

---
Avg Pool

---
Classifier