SHViT zerlegt

---
16x16 Overlap PatchEmbebed
256 x 256 x 28
32 x 32 x 224
Probe: 32*16 = 512
128 x 128 x 56
64 x 64 x 112
3x3 kernel
Stride = 2
BN
Activation = ReLU
3x3 kernel
Stride = 2
BN
Activation = ReLU
3x3 kernel
Stride = 2
BN
Activation = ReLU
3x3 kernel
Stride = 2
BN
Activation = ReLU
512 x 512 x 3
16x16 Overlap Patch Embed
3x3 strided Conv
3x3 strided Conv
3x3 strided Conv
3x3 strided Conv
[Speaker Notes: 10 - LeViT: a Vision Transformer in ConvNet’s Clothing for Faster Inference: Nutzen auch „4 layers of 3 × 3 convolutions (stride 2)” For LeViT, each convolution is followed by a batch normalization 27 - EfficientViT: Memory Efficient Vision Transformer with Cascaded Group Attention ====================================== - ViT zerlegt das Eingabebild in p×p non-overlapping Patches, die als Eingabe für den Transformer-Encoder dienen. Dies wird standardmäßig mit einer p×p-convolution mit Stride p=16 umgesetzt ====================================== 32 - Early Convolutions Help Transformers See Better Convolutional stem details Our convolutional stem designs use four […] 3×3 convolutions “The output channel“ is “[64, 128, 128, 256, 256, 512]“# All 3×3 convolutions are followed by batch norm (BN) [21] and then ReLU [29]]

---
Stage 1
3x3 DW Conv
Feed Forward Network
3x3 kernel
Stride = 1
BN (fused)
Activation = ReLU
Stride = 1
Padding = 0
BN (fused)
Activation = ReLU
Fully Connected
32 x 32 x 224
32 x 32 x 224
[Speaker Notes: Batch Normalization ----------------------- Im Bild wird erwähnt, dass Batch Normalization in Convolution Layers integriert (fused) werden kann Während des Trainings wird BN normal verwendet (normalisiert die Ausgabe der Convolution), um die Aktivierungen zu stabilisieren. Wo BN verwendet wird: - In der Abbildung wird BN klar an den Stellen gezeigt, wo 3x3 Depthwise Convolution vorkommt (Stage 1 bis Stage 3) - Für andere Schichten, wie die Feedforward Layers, wird BN verwendet, sofern sie keine Self-Attention-Layer sind. ============================================================================ Stage 1 wird L1 (depth=4) mal hintereinander gesetzt 10 - LeViT: a Vision Transformer in ConvNet’s Clothing for Faster Inference: - The ViT uses layer normalization before each at- tention and MLP unit - For LeViT, each convolution is followed by a batch normalization - The batch normalization can be merged with the preceding convolution for inference, which is a runtime advantage over layer Normalization 27 - EfficientViT: Memory Efficient Vision Transformer with Cascaded Group Attention 28 - MetaFormer Is Actually What You Need for Vision 29 - Rethinking Mobile Block for Efficient Attention-based Models 32 - Early Convolutions Help Transformers See Better 52 - Batch Normalization: Accelerating Deep Network Training by Reducing Internal Covariate Shift]

---
FFN
Feed Forward Network
Conv2D
Conv2D
ReLU
1x1 pointwise convolution
BN
1x1 pointwise convolution
BN
Input (batch_size, height, width, ed)
Output (batch_size, height, width, ed)
(1, 32, 32, 224)
(1, 32, 32, 224)
[Speaker Notes: Input (batch_size, height, width, ed) ↓ Conv2d_BN (pw1, 1x1, filters=h) ↓ ReLU Conv2d_BN (pw2, 1x1, filters=ed) ↓ Output (batch_size, height, width, ed)]

---
DownSample 1-2
(1, 16, 16, 256)
Downsample
(1, 32, 32, 128)
Input (batch_size, height, width, channels)
Patch Merging
Output (batch_size, height/2, width/2, out_dim)
(1, 16, 16, 256)
(1, 16, 16, 256)
(1, 32, 32, 128)
3x3 DW Conv
Feed Forward Network
3x3 DW Conv
Feed Forward Network
[Speaker Notes: 00 - SHViT Single-Head Vision Transformer with Memory Efficient Macro Design To reduce tokens without information loss, we utilize an efficient downsampling layer, which is composed of two stage 1 blocks, with an inverted residual block [27,50,51] (stride-2) placed between them Auf Deutsch: - Der Downsampling Layer besteht aus 2 Stages von Typ “Stage 1” mit einem ”inverted residual block” (PatchMerging (strides=2)) ================================================ Stage 1 --------- DW Conv + FFN ================================================ 2.5 cm 3.3 cm]

---
Patch Merging
Conv2D BN
3x3 DW Conv
3x3 DW Conv
ReLU
SqueezeExcite
1x1
filters=hid_dim(=dim * 4))
3x3
Depthwise
strides=2
Padding=same
1x1
filters=out_dim
Input (batch_size, height, width, channels)
Output (batch_size, height/2, width/2, out_dim)
[Speaker Notes: # https://arxiv.org/pdf/1709.01507 Input (batch_size, height, width, channels) ↓ Conv2d_BN (conv1, 1x1, filters=hid_dim) ↓ ReLU Conv2d_BN (conv2, 3x3, depthwise, strides=2) ↓ ReLU Squeeze-and-Excitation (SE) ↓ Conv2d_BN (conv3, 1x1, filters=out_dim) ↓ Output (batch_size, height/2, width/2, out_dim) block1 in : (1, 32, 32, 224) block1 out: (1, 32, 32, 224) ================================================ ### PatchMerging ### (1, 32, 32, 224) (1, 16, 16, 336) ============================== ### PatchMerging ### (1, 32, 32, 224) (1, 16, 16, 336) ============================== block2 out: (1, 16, 16, 336) ### PatchMerging ### (1, 16, 16, 336) (1, 8, 8, 448) ============================== ### PatchMerging ### (1, 16, 16, 336) (1, 8, 8, 448) ============================== block3 out: (1, 8, 8, 448)]

---
Stage 2
3x3 DW Conv
Feed Forward Network
Single Head Attention
Layer Normalization
Group Normalization
ReLU activation
16 x 16 x 336
16 x 16 x 336
[Speaker Notes: Stage 2 wird L2 (depth=7) mal hintereinander gesetzt # https://github.com/ysj9909/SHViT/blob/main/model/shvit.py Stage 1: block1 in: (1, 32, 32, 224) block1 out: (1, 16, 16, 336) [wegen Downsampling  andere Shapes] Stage 2: block2 in : (1, 16, 16, 336) block2 out: (1, 8, 8, 448) [wegen Downsampling  andere Shapes] Stage 3: block3 in: (1, 8, 8, 448) block3 out: (1, 8, 8, 448) Stage 1: block1 in : (1, 32, 32, 224) block1 out: (1, 32, 32, 224) Stage 2: block2 in : (1, 32, 32, 224) ### PatchMerging ### (1, 32, 32, 224) (1, 16, 16, 336) ============================== ### PatchMerging ### (1, 32, 32, 224) (1, 16, 16, 336) ============================== block2 out: (1, 16, 16, 336) Stage 3: block3 in : (1, 16, 16, 336) ### PatchMerging ### (1, 16, 16, 336) (1, 8, 8, 448) ============================== ### PatchMerging ### (1, 16, 16, 336) (1, 8, 8, 448) ============================== block3 out: (1, 8, 8, 448)]

---
Single-Head-Attention
x2
x1‘
em_dim – part_dim (x2)
part_dim (x1)
GroupNorm
V
K
Q
Self - Attention
Identity
C
Output Projection
(1,16,16,336)
(1,16,16,336)
[Speaker Notes: # https://github.com/ysj9909/SHViT/blob/main/model/shvit.py Input Tensor (B, H, W, dim) ↓ Split along channel dimension: [pdim, dim - pdim] ↓	↓ x1 (B, H, W, pdim)	x2 (B, H, W, dim - pdim) ↓ GroupNorm (x1) → Normalized Tensor ↓ Conv2d_BN → qkv projection ↓ Split into q, k, v tensors: q: (B, H*W, qk_dim) k: (B, H*W, qk_dim) v: (B, H*W, pdim) ↓ Attention computation: attn = (q @ k^T) * scale ↓ Softmax over attention scores ↓ Weighted sum: v @ attn^T → (B, H*W, pdim) ↓ Reshape to spatial dimensions: (B, H, W, pdim) ↓ Concatenate with x2 (B, H, W, dim) ↓ Projection Layer: ReLU + Conv2d_BN ↓ Output Tensor (B, H, W, dim)]

---
Tensor Shapes
Stages	Shapes	Shapes (with numbers)
Input Tensor	(B,H,W,dim) -> [1,32,32,224]	Batch size = 1, spatial dimensions = 32×32, channels = 224
After Split / Channel Split	x1: (B,H,W,p_dim) -> (1,32,32,48) / x2: (B,H,W,dim-p_dim) -> (1,32,32,176)	x1: (pdim=48) / x2: (dim−pdim=224−48=176)
GroupNorm on x1	(B,H,W,p_dim) -> [1,32,32,48]	Normalize x1​ across its 48 channels
QKV Projections	Q: (B,H∗W,qk_dim) -> [1,32,32,48] / K: (B,H∗W, qk_dim) -> [1,32,32,48] / V: (B,H∗W, p_dim) -> [1,32,32,48]	~ nochmal nachschauen
Flatten Spatial Dimensions	QKV: [1,1024,48]	Spatial dimensions (32×32 = 1024) are flattened
Attention Scores	(B,H∗W,H∗W) -> [1,1024,1024]	Compute scaled dot-product attention: q @ k^T
Softmax over Attention Scores	(B,H∗W,pdim) -> [1,1024,1024]	Apply Softmax across the last dimension
Weighted Sum	(B,H,W,pdim) -> [1,1024,48]	Attn_score * v^T = attn@v^T
Reshape Weighted Values	[1,32,32,48]	Reshape the outpzt back to spartial dimensions
Concatenated Tensor	(B,H,W,dim) -> [1,32,32,224]	Concatenate the processed x1 [1,32,32,48] with x2​ [1,32,32,176]
Projection Layer / Final Output	(B,H,W,dim) -> [1,32,32,224]	Apply ReLU and Conv2D to combine features into the final output tensor

---
DownSample 2-3
(1, 8, 8, 384)
Downsample
Input (batch_size, height, width, channels)
Patch Merging
Output (batch_size, height/2, width/2, out_dim)
(1, 8, 8, 384)
(16 x 16 x 256)
(1, 8, 8, 384)
3x3 DW Conv
Feed Forward Network
3x3 DW Conv
Feed Forward Network
[Speaker Notes: 00 - SHViT Single-Head Vision Transformer with Memory Efficient Macro Design To reduce tokens without information loss, we utilize an efficient downsampling layer, which is composed of two stage 1 blocks, with an inverted residual block [27,50,51] (stride-2) placed between them Auf Deutsch: - Der Downsampling Layer besteht aus 2 Stages von Typ “Stage 1” mit einem ”inverted residual block” (PatchMerging (strides=2)) ================================================ Stage 1 --------- DW Conv + FFN ================================================ 2.5 cm 3.3 cm]

---
Stage 3
3x3 DW Conv
Feed Forward Network
Single Head Attention
8x8x384
8x8x384
[Speaker Notes: Stage 2 wird L2 (depth=7) mal hintereinander gesetzt Stage 1: block1 in : (1, 32, 32, 224) block1 out: (1, 32, 32, 224) Stage 2: block2 in : (1, 32, 32, 224) ### PatchMerging ### (1, 32, 32, 224) (1, 16, 16, 336) ============================== ### PatchMerging ### (1, 32, 32, 224) (1, 16, 16, 336) ============================== block2 out: (1, 16, 16, 336) Stage 3: block3 in : (1, 16, 16, 336) ### PatchMerging ### (1, 16, 16, 336) (1, 8, 8, 448) ============================== ### PatchMerging ### (1, 16, 16, 336) (1, 8, 8, 448) ============================== block3 out: (1, 8, 8, 448)]

---
Avg Pool
x = torch.nn.functional.adaptive_avg_pool2d(x, 1).flatten(1) +
[Line 222]

---
Classifier
Line 211 – 215
https://github.com/ysj9909/SHViT/blob/main/model/shvit.py
FFN

---
Offene Fragen / Todos
Warum wird Patch Merging fürs Downsampling verwendet?
Warum dieser Partial Anteil?
Was macht der Identity Layer?
Was muss ich zu Batch / Group Normalization wissen?
Was macht ein 1x1 Kernel Block
https://github.com/ysj9909/SHViT/blob/main/model/shvit.py

---
Weiteres Vorgehen
https://arxiv.org/pdf/2105.15203 (SegFormer: Simple and Efficient Design for Semantic Segmentation with Transformers)
Shapes sind nicht ganz richtig:
Richtig wäre:
  - Nach Patch Embedding: (1,128,32,32)
  - Nach Stage 1: (1,128,32,32)
  - Nach Downsampling_12: (1,256,16,16)
  - Nach Stage 2: (1,256,16,16)
  - Nach Downsampling_23: (1,384,8,8)
  - Nach Stage 3: (1,384,8,8)

---
MLP – Decoder

---
MLP (Linear Embedding)
8x8x448

---
Upsample